## Slide 1
Full UVM Testbench for
AHB to APB Bridge Design
DIGITAL VERIFICATION
Supervisor Eng. Omar Younis
AHB to APB Bridge UVM Project

## Slide 2
Agenda
1- Role of each member
2- Testbench Architecture
3- AHB Agent
4- APB Agent
5- Scoreboard
6- Assertions
7- Covergroups
8- Coverage Closure
AHB to APB Bridge UVM Project
2

## Slide 3
3
Name | Primary Ownership | UVM Implementation
Marwa | AHB | AHB Agent
Abdelrahman | APB | APB Agent
Menna | Assertions + CDC + Reset | Top + reset + Assertions
Sameh | Bridge/Data Integrity | Env + Scoreboard + Reference Model + Tests
Roaa | Tests + Coverage Strategy | Sequences + Covergroups
Role of Each Member
AHB to APB Bridge UVM Project

## Slide 4
AHB to APB Bridge UVM Project
4
UVM Architecture

## Slide 5
1. Sequencer
Manages the delivery of AHB sequence items to the driver.
AHB Master Agent
2. Driver
Drives AHB address & control and write-data signals, handles transfer handshaking and wait states, and captures read data and response status.
3. Monitor
Passively detects accepted AHB transfers, collects address/control and data/response information, counts wait states, and publishes completed transactions.
4. Configuration
Stores the AHB virtual interface and the active/passive mode, allowing the agent and its components to access shared configuration.
5. AHB Interface
Defines the AHB signals and driver/monitor clocking blocks to coordinate signal driving and sampling on HCLK
AHB to APB Bridge UVM Project
5

## Slide 6
Driver's Job
AHB Driver
The driver takes ahb_item transactions from the sequencer and drive them on the ahb interface.It keeps the AHB pipeline full, so the address of the next transfer goes out while the data of the current one is still on the bus. It holds everything when the slave pulls HREADY low, stores HRDATA and HRESP back into the item, and handles reset
Two transfers, A then B. In cycle 2 the bus carries B's address while A's data is still on the bus, so the driver keeps track of two transfers at once.
AHB to APB Bridge UVM Project
6

## Slide 7
addr_item
data_item
The transfer whose address is on the bus now
The transfer whose datais on the bus now
Every clock cycle
Reset?
Abort: item_done on the open item, clear both boxes, initialize the bus.
Drive the address
try_next_item, then drive_addr.
No item? drive_idle.
Drive the data
If data_item is a write, put its HWDATA on the bus.
Wait for the clock
@(drv_cb), then look at HREADY.
need an item?? try_next_item never blocks, so the bus sees an idle cycle instead of a stall
AHB Driver
AHB to APB Bridge UVM Project
7

## Slide 8
AHB Driver
HREADY decides
HREADY = 1
Slave accepted the phase.
addr_item: if HTRANS[1], it becomes data_item (wait_states = 0). item_done, clear addr_item.
HREADY = 0
Slave is stalling.
Hold everything on the bus. addr_item stays non-null, so it is driven again next cycle.
data_item: wait_states++.
Boxes only move forward on HREADY = 1, so a stall never loses or reorders a transfer
AHB to APB Bridge UVM Project
8

## Slide 9
AHB Monitor
Reset drops pending_item and clears wait_states. One item goes out per completed transfer
Catch the address
HREADY, HSEL and HTRANS[1] all high: create an item (current_item) with HADDR, HWRITE, HTRANS, HSIZE, HPROT. then mark it as pending_item.
Count the stalls
While HREADY = 0 the data phase is not finished: wait_states++.
Publish it
HREADY = 1: fill HWDATA, HRDATA, HRESP and wait_states, then ahb_aport.write(pending_item).
AHB to APB Bridge UVM Project
9

## Slide 10
AHB Interface
Clocking block
Synchronizes signal driving and sampling with the AHB clock (HCLK).
drv_cb: Controls when the driver drives signals and samples responses.
mon_cb: Allows the monitor to sample AHB signals consistently.
Helps avoid race conditions between the testbench and DUT.
AHB to APB Bridge UVM Project
AHB to APB Bridge UVM Project
10

## Slide 11
AHB to APB Bridge UVM Project
11
Slave responder
The DUT acts as APB master.
The agent answers it by driving
PREADY, PRDATA and PSLVERR.
Reactive
The DUT acts as APB master.
The agent answers it by driving
PREADY, PRDATA and PSLVERR.
APB Agent

## Slide 12
AHB to APB Bridge UVM Project
12
APB Agent
Component
Class
is_active flag and virtual apb_if
apb_config
Samples request and completed transfer
apb_monitor
Job
Stores requests in request_fifo
apb_sequencer
Drives the slave response signals
apb_driver
Waits for a request, then randomizes a response
apb_sequence
Config
Monitor
Sequencer
Driver
Sequence

## Slide 13
APB Agent
Reactive data flow
Monitor
Sequencer
Detects setup phase (PSEL=1, PENABLE=0) and publishes the request on request_aport.
request_export feeds request_fifo inside the sequencer.
1
2
Sequence
Gets one request, creates apb_response, and randomizes it.
3
Driver
Takes the response access phase at(PSEL=1, PENABLE=1) with get_next_item and drives it on the bus.
4
AHB to APB Bridge UVM Project
13

## Slide 14
AHB to APB Bridge UVM Project
14
APB Transaction Classes
sequence_item (observed)
apb_response (random)
Request fields: PADDR, PWRITE, PWDATA, PSTRB,
PPROT, PSEL, PENABLE, APBACTIVE.
Filled at completion: PRDATA, PSLVERR, wait_count.
PRDATA (32 bits), PSLVERR, and wait_cycles constrained inside [0:5]. This is what the sequencer hands to the driver.

## Slide 15
AHB to APB Bridge UVM Project
15
Driver and monitor timing
  Driver waits on posedge PCLK until PSEL and PENABLE are both high (access phase).
2. It holds PREADY low for wait_cycles clock cycles.
3. It sets PREADY=1 with PRDATA and PSLVERR for one cycle, then clears them.
4. The monitor counts cycles with PREADY low, then publishes the finished item on transaction_aport.
5. A clocking block in apb_if times all sampling and driving to the clock, which removes the race between the .. testbench and the DUT.

## Slide 16
AHB to APB Bridge UVM Project
16
Scoreboard & Golden Model

## Slide 17
1. Inputs
Two analysis exports: ahb_aexport and apb_aexport, fed by the agents
2. Predictors
ahb_prd and apb_prd turn each observed transaction into the expected one
3. Comparator
Matches expected against actual, counts passes and failures, prints a report
Scoreboard structure
AHB to APB Bridge UVM Project
17

## Slide 18
Expected AHB | Taken from APB
HREADYOUT | PREADY
HRESP | PSLVERR
HRDATA | PRDATA
  Every APB item produces one expected AHB item, sent through ahb_exp_aport.
AHB Predictor
AHB to APB Bridge UVM Project
18

## Slide 19
Expected APB | Mapping
PADDR | HADDR[15:2]
PWRITE / PWDATA | Copied from HWRITE / HWDATA
PPROT | Remapped from HPROT bits
PSEL | HSEL and HTRANS[1]
PSTRB | From HSIZE and HADDR[1:0] on writes, else 0
  Only items with PSEL high are sent on to the comparator.
APB Predictor
AHB to APB Bridge UVM Project
19

## Slide 20
Collect
Four analysis FIFOs: expected and actual, for AHB and for APB
Compare
run_phase takes one item from each FIFO and calls compare on each pair
Report
Pass and fail counts with pass rate per bus, then an overall verdict
Comparator
19
AHB to APB Bridge UVM Project
20

## Slide 21
Assertions
AHB to APB Bridge UVM Project
21
1. Phases legality
SETUP/ACCESS legality, PREADY completion, signals stable during wait states
2. AHB to APB tracking
No phantom or duplicate APB request for an accepted AHB transfer
  CDC handshake
Four req/ack ordering checks ported from the DUT OVL assertions to SVA
4. Data and response
HRDATA = PRDATA, HRESP = PSLVERR, PWDATA = HWDATA on writes, APBACTIVE high when needed

## Slide 22
Assertions - phases legality
  $rose(PSEL) |-> !PENABLE
  PENABLE |-> PSEL
  apb_setup |=> (apb_access and p_apb_ctrl_stable)
  (apb_access && !PREADY) |=> apb_access
  (apb_access && !PREADY) |=> p_apb_ctrl_stable
  apb_done |=> !PENABLE
AHB to APB Bridge UVM Project
22

## Slide 23
AHB Counter
@(posedge HCLK)
ahb_acc_cnt
the bridge must preserve a one-to-one relationship between accepted AHB transfers and APB transfer starts, even though the two interfaces use different clocks.
Assertions - AHB to APB tracking
if ( ahb_accept)
ahb_acc_cnt ++;
Compare Counters
  APB SETUP needs a pending AHB request
apb_setup |-> (apb_start_cnt < ahb_acc_cnt)
APB Counter
@(posedge PCLK)
apb_start_cnt
if ( apb_setup)
apb_start_cnt ++;
  When the AHB side completes (HREADYOUT = 1) the counters must match.
$rose(HREADYOUT) |-> (apb_start_cnt==ahb_acc_cnt)
AHB to APB Bridge UVM Project
23

## Slide 24
Assertions - CDC Handshaking
  Req may only rise when Ack is low
$rose(s_req_h) |-> !s_ack_h)
  Req may only fall when Ack is high
$fell(s_req_h) |-> s_ack_h)
  Ack may only rise when Req is high
$rose(s_ack_p) |-> s_req_p)
  Ack may only fall when Req is low
$fell(s_ack_p) |-> !s_req_p)
AHB to APB Bridge UVM Project
24

## Slide 25
Assertions - Data & Response
Check | What is verified
Read data | HRDATA equals the last APB read data (OKAY responses only)
Response | HRESP equals the last PSLVERR when the transfer completes
Write data | On APB writes, PWDATA equals the last accepted AHB write data (reads are not checked)
APBACTIVE | High whenever req and ack differ, and whenever PSEL=1
AHB to APB Bridge UVM Project
25

## Slide 26
Assertions Results
AHB to APB Bridge UVM Project
26

## Slide 27
AHB Transfer Coverage
AHB to APB Bridge UVM Project
27
CG-001–004, CG-009–010 | Coverage of AHB request attributes
Transfer attributes
HWRITE: READ / WRITE
HTRANS: NONSEQ / SEQ
HSIZE: BYTE / HALFWORD / WORD
Address regions
LOW
0000–5555
MID
5556–AAAA
HIGH
AAAB–FFFF
Protection attributes
HPROT[1:0]
BIN
00
BIN
01
BIN
10
BIN
11
Read/Write × Transfer Size | Cross coverage
Each cell is a required combination
BYTE
HALFWORD
WORD
READ
Covered combination
Covered combination
Covered combination
WRITE
Covered combination
Covered combination
Covered combination
The cross combines:
• 2 transfer directions
• 3 supported transfer sizes
• 6 total combinations

## Slide 28
APB Transfer Coverage
CG-005–008, CG-013 | Strobes, completion, response and latency
PSTRB patterns
Observed APB byte enables.
NO STROBE
0000
BYTE 0
0001
BYTE 1
0010
BYTE 2
0100
BYTE 3
1000
HALFWORD LOW
0011
HALFWORD HIGH
1100
FULL WORD
1111
APB response
PSLVERR
OKAY | 0
PSLVERR
ERROR | 1
PREADY = 1 at published completion
SETUP: PSEL = 1, PENABLE = 0
Transfer latency | wait_count bins
NO WAIT
wait_count = 1
ONE WAIT
wait_count = 2
2–3 WAITS
wait_count = 3–4
4+ WAITS
wait_count = 5+
AHB to APB Bridge UVM Project
28

## Slide 29
End-to-End Cross Coverage
CG-011, CG-012 | Link the AHB request attributes to the APB outcome
Read/Write × APB response
Sampled only after an AHB/APB pair is matched
OKAY
ERROR
READ
Combination bin
Combination bin
WRITE
Combination bin
Combination bin
Read/Write × Wait × Response
Three dimensions create 8 combinations:
DIRECTION
READ / WRITE
×
LATENCY
NO WAIT / WAIT
×
RESPONSE
OKAY / ERROR
Goal: exercise every observed combination of transaction direction, APB latency category, and response status.
Cross coverage is sampled only for address-matched pairs.
Transaction pairing check
The component compares AHB HADDR[15:2] with APB PADDR[15:2] before sampling the cross groups.
AHB to APB Bridge UVM Project
29

## Slide 30
Waived item | Type | Justification
Synchroniser enable (both instances) and its all-false branch | Toggle, branch | Tied to 1 in design
HSIZE[2] | Toggle | Maximum data width is 32 bits
PPROT[1] | Toggle | Always 0 in the RTL mapping
PADDR[1:0] | Toggle | always “00”, APB address is always word-aligned
FSM default branches and illegal state (both FSMs) | Line, FSM state | Unreachable default / illegal encodings
Unaligned-address branches | Line | Unaligned transfers are not legal AHB stimulus
Coverage Exclusions
AHB to APB Bridge UVM Project
30

## Slide 31
Coverage Closure: Added Tests
Reset while an AHB transfer is in flight
Reset in APB SETUP / ACCESS phase
HPROT, HTRANS different values
Reset on one side only
(HRESETn or PRESETn)
AHB to APB Bridge UVM Project
31

## Slide 32
AHB to APB Bridge UVM Project
32
Coverage results

## Slide 33
Thank You
Any Questions?
AHB to APB Bridge UVM Project
33